NuVi, an automobile navigation device by Garmin, treat marine navigation symbols differently than Garmin GPS that were intended for marine navigation.  As such, some NuVis (especially ones manufactured since 2010) may not display Bizer’s data properly.

This can best be illustrated by three examples using four Garmin GPS:

- The area surrounding the Witches between Governor’s Island and Timber Island.

  - http://www.bizer.com/garmin/1211319_Garmin.jpg - Small

http://www.bizer.com/garmin/121131c_Garmin.jpg - Large

- The area in the vicinity of the Long Island Bridge

  - http://www.bizer.com/garmin/1211329_Garmin.jpg - Small

http://www.bizer.com/garmin/121132c_Garmin.jpg - Large

- The area known as The Graveyard

  - http://www.bizer.com/garmin/1211339_Garmin.jpg - Small

http://www.bizer.com/garmin/121133c_Garmin.jpg - Large

In each of these photographs, there are four Garmin GPS.

- The upper-left is a 2011 NuVi 50LM

- The upper-right is a 2006 GPSMAP 276C (what I use around the lake)

- The lower-left is a 2011 NuVi 2360LMT

- The lower-right is a 2008 NuVi 750W (an older GPS that works well)

Comments on Bizer’s observations (your observations may be different)

- “Newer” NuVis (the two on the left) do display the shoals (dark blue) quite well, but that’s where the “good” ends.  The shoals of the two newest NuVis cover a portion of Whortleberry Island for some reason.

- Newer NuVis don’t display buoys or rocks until you’re right on top of them and the device is zoomed way in.  In other words, you’ll see the buoys on the water before you see them on the GPS.  In the photos, the two newer NuVis are missing all the buoys in the Witches.

- In newer NuVis, when a buoy is displayed, what you see is a rectangle (or square) with a buoy symbol inside the rectangle.  While the buoy symbol can be anywhere within the rectangle, the actual location of the buoy on the water is depicted by the center of the rectangle, not the buoy symbol itself.  In addition, the rectangle hides anything that might be “under” the rectangle.

- With newer NuVis, many symbols appear about 1/8 inch north of where they are actually located.

- Note that the 50LM fails to show any depth contours or the suggested boating route (dashed or magenta lines)

- The older NuVi doesn’t show the shoals very well (one really has to look closely).  Other than that, it appears to work quite well.

- It’s too bad that Garmin no longer makes the 276C.  That’s my favorite.